## Slide 1
IA736001 INTERNET OF THINGS AND CLOUD COMPUTING
Two-Node ESP-NOW Sensor Network
with a ThingsBoard Cloud Gateway
A mesh-ready packet design demonstrated over a single hop
Bhanu Gupta · Roshan Aryal | 9 September 2026
Notes: 10 minutes total, then 5 for questions. Names and course code on this slide before you present. Have both boards powered and the dashboard already open.

## Slide 2
WHY THIS EXISTS
The problem
A sensor is somewhere without Wi-Fi coverage, mains power, or both.
- Wi-Fi association costs seconds and milliamps before a single byte moves
- Every node needing its own AP credentials does not scale
- One connected gateway can carry data for several local nodes
So: cheap radio between the nodes, one gateway that owns the cloud link.
Notes: Frame the problem before the solution. The point is that a sensor with no network connection of its own still gets its data to the cloud.

## Slide 3
SCOPE
What we built
Board 1 - Remote node
DHT11 on GPIO4. Reads and transmits every 5 s over ESP-NOW. Never joins the access point.
Board 2 - Gateway
DHT11 on GPIO5. Joins eduroam, receives and deduplicates Board 1's packets, merges both readings, publishes to ThingsBoard over MQTT every 10 s.
No wire between the two boards. The only link is a 2.4 GHz radio.
Two-node prototype with a mesh-ready packet design - not a demonstrated multi-hop mesh. Two radios can only ever be one hop.
Notes: Hold the boards up here. Physically separate them so the audience sees there is no wire. Say the scope claim now, not at the end.

## Slide 4
NETWORKING
Architecture
Notes: Walk left to right. Two protocols doing two different jobs: ESP-NOW has no IP stack at all, MQTT is TCP to the cloud.

## Slide 5
WIRING
Circuit

## Slide 6
THE GOVERNING CONSTRAINT
One radio, one channel
An ESP32 has a single radio, so it is on exactly one channel at a time.
The gateway must join Wi-Fi for the cloud - and the access point decides which channel that is.
So the channel is discovered at runtime, never chosen at design time.
- The node is pinned to that channel by hand, and reads it back to confirm
- The node never associates - association would let the two boards drift apart
- Gateway must be flashed and running before the node can even be configured
Notes: This is the best thing you have to explain and it is worth dwelling on. The channel is discovered, not chosen. It dictates the whole upload order.

## Slide 7
26 BYTES
Packet design
version, msg_type protocol evolution
src_id, dst_id addressing, not broadcast
boot_id random per power-up
seq ordering within a session
ttl, hop_count carried, never decremented
temperature, humidity the payload
uptime_ms sender liveness
Why no checksum?
802.11 already CRC-checks every delivered frame. A checksum would duplicate hardware work - and would not authenticate anything.
static_assert(sizeof == 26)
Pins the size in both sketches. It constrains layout but does not prove field agreement - fields could be reordered and still pass.
Notes: 26 bytes against a 250-byte limit. Point out ttl and hop_count are carried but never decremented - that is the mesh-ready part, and it is honest to say so.

## Slide 8
SOFTWARE
Deduplication
Key: (src_id, boot_id, seq)
Strict last-sequence-wins. Anything not newer than the highest already accepted in this session is a duplicate.
boot_id is randomised every power-up.
Without it, a node restart looks identical to a replay: every packet arrives with a sequence below the stored baseline and is rejected forever. The node never comes back.
A forward jump is a gap, not a duplicate - those packets were lost, not repeated. A receiver demanding contiguous sequences would deadlock on the first loss.
Notes: boot_id is the part worth explaining. Without it a node restart is indistinguishable from a replay and the node never comes back.

## Slide 9
THREAT MODEL
Security
Defended
+ Length, version, type, addressing, range validation
+ Replay rejection via sequence numbers
+ ESP-NOW encryption + sender auth - PMK + per-peer LMK
+ Sender MAC filtering (defence in depth)
+ Credentials excluded from version control
Not defended
- MQTT without TLS - token in clear text
- RADIUS certificate not validated
- Credentials readable from flash over USB
The interesting finding
src_id is a claim, not proof. A forged packet with a high sequence number under the live boot_id advances the dedup baseline - after which every genuine packet is rejected until the node reboots. Replay protection becomes the attack surface. Fixed by encrypting the link: a MAC filter was not enough, because the attacker controls the value being filtered on.
Notes: Security is 25 marks with the other domains. Lead with the attack you found yourselves - that reads far better than a list of things you did not do.

## Slide 10
MEASURED
Results
634 packets received and validated
82 duplicates rejected
0 invalid packets - both boards agree on the 26-byte layout
14 / 14 acceptance criteria evidenced
Node offline detection latches at 20 s; last known value keeps publishing while node1_online carries the truth about freshness.
Notes: Numbers from evidence/01_gateway_running_state.txt. invalid=0 across 634 packets is the one to point at - it proves both boards agree on the packet layout.

## Slide 11
CLOUD
Edge aggregation, visualised
Blue: gateway local sensor. Green: remote node, via ESP-NOW. Stepped traces are DHT11 quantisation, not a frozen sensor.
Notes: This is the money shot. Two physically separate sensors, one of which has no network connection, arriving as a single cloud stream.

## Slide 12
BOTH DIRECTIONS
Control and resilience
Telemetry alone makes a device observable. It does not make it manageable.
The gateway subscribes to v1/devices/me/rpc/request/+ and replies on the matching response topic. Three methods: getStatus, setPublishInterval, resetCounters.
Verified end to end - a dashboard button produced the request in the gateway log, the applied change, and the new interval back in the next telemetry message. The round trip, not just the request.
setPublishInterval range-checks and rejects rather than clamping. Silently applying a value the operator did not ask for would leave them believing something untrue about the device.
Unsent payloads go to a twelve-slot ring buffer and flush oldest-first on reconnect. Measured: 4 buffered, 4 flushed, 0 dropped.

## Slide 13
SWITCH TO HARDWARE
Live demonstration
1. Board 1 serial: no Wi-Fi association, and a real link-layer ack
2. Board 2 serial: the same packet arriving, validated, deduplicated
3. ThingsBoard: the same numbers, in the cloud
4. Warm the sensor by hand and watch the chart move
5. Unplug Board 1: node1_online goes false after 20 s
Roughly 21 C to 28 C in fifteen seconds - it proves the whole chain, sensor to cloud, in one gesture.
Notes: SWITCH TO LIVE. Three windows: both serials and the dashboard. Warm the sensor with your thumb - about 7 degrees in 15 seconds, and it relaxes back after.

## Slide 14
HARDWARE SUBSTITUTION
DHT11 instead of BMP280
The brief specified BMP280. The available hardware was DHT11.
Lost
- No I2C experience - DHT11 is single-wire bit-banged
- Lower resolution, hence the stepped chart traces
Gained
- Humidity responds to a hand in seconds; indoor pressure would be flat for hours
- Everything above the sensing layer is unchanged - the packet carries two floats and does not care what they represent
Notes: Own the substitution rather than hiding it. The gain is real: indoor pressure would be a flat line for hours, humidity responds to a hand in seconds.

## Slide 15
HONESTLY
Limitations
- One hop only - two radios cannot demonstrate multi-hop forwarding
- ttl and hop_count are designed for but unexercised
- MQTT without TLS - the radio leg is encrypted, the cloud leg is not
- Credentials compiled into firmware, recoverable over USB
- Manual channel configuration - a gateway roam silently breaks the link
- Single remote node - dedup state is one slot, not an array
Notes: Name these yourself. Being asked about a limitation you did not mention is worse than raising it first.

## Slide 16
MEASURED, NOT ASSUMED
What we found
Port 1883 is open outbound on eduroam
Proved by the MQTT return code: state=5 is a reply from the broker, so the packets crossed the firewall. state=-2 would have meant no TCP connection at all.
WPA2-Enterprise costs ~97 KB of flash
915,267 bytes with PSK against 1,012,651 with PEAP. Enterprise auth is not free.
eduroam routes by RADIUS realm, not email domain
user@student.<institution> failed; user@<institution> worked. The failure is silent - the same status code as a wrong password.
Notes: These are yours - measured, not read in a datasheet. Worth saying that explicitly.

## Slide 17
WHAT WOULD COME NEXT
Further work
1. A third node - actually exercise ttl and hop_count
2. MQTT over TLS on port 8883
3. Credentials provisioned into NVS at first boot, not compiled in
4. Automatic channel recovery instead of a manual re-upload
5. Persist the buffer to NVS so it survives a reboot, not just a reconnect
Notes: Short. Shows you know what production would need.

## Slide 18
Questions
Two ESP32 boards. No wire between them. Two sensors, one cloud stream.
Code, evidence and full report: github.com/bhanuGupta1/esp32-espnow-thingsboard-gateway
Notes: Stop here and take questions. Rehearsed answers are in DEMO_PLAN.md - especially the security one, which is the likeliest question.